Alexander Hay
ME333 - Mechatronics
Chapter 7, 1-2
Chapter 8, 1
Chapter 9, 1
Chapter 10, 1-2

7.1	False
“if an input pin is not connected to anything, we cannot be certain what the input will read.”
pg. 116

7.2	a	Pin 2 will most likely have an external pull-up resistor.
500Ω-100kΩ. At 5V, currents below 50 μA will not be read as logic high. 10mA is the	most current the pin can receive at 5V. 9V 900Ω

b	AD1PCFG = 0x1E;
TRISBbits.TRISB1 = 0;
TRISBbits.TRISB2 = 0;
TRISBbits.TRISB3 = 1;
TRISBbits.TRISB4 = 1;
TRISB = 0x18	// does this do the same thing?

ODCBbits.ODCB1 = 0;
ODCBbits.ODCB2 = 1;
ODCBbits.ODCB3 = 0;
ODCB = 0x4;

CNPUEbits.CNPUE4 = 1;
CNCONbits.ON = 1;
CNENbits.CNEN3 = 1;

8.1	T3CON = 0x8060;
PR3 = 0x4E1F;

9.1	f_pwm = 80,000 / 2^{n}

RC = f_pwm / ( 80%pi)

10.1	AD1CON1bits.SRCC = 0x111;
AD1CON1bits.ASAM = 0;
AD1CON1bits.ADCS =
Tad = 6*Tpb = 75ns
Tsamp = 2*Tad = 150ns

10.2	unsigned int adc_sample_convert(int pin) {	// sample & convert the value	// on the given
// adc pin the pin should be	// configured as an
// analog input in AD1PCFG
unsigned int elapsed = 0,
finish_time = 0;
AD1CHSbits.CH0SA = pin;	// connect chosen pin to MUXA for
// sampling
elapsed = _CP0_GET_COUNT();
finish_time = elapsed + 10;	// 10 core timer ticks = 250 ns
while (_CP0_GET_COUNT() < finish_time) {
;	// sample for more than 250 ns
}
return ADC1BUF0;	// read the buffer with the result
}